## Slide 1
Track C
Low-Level Networking
& Kernel Development
XDP • TC • eBPF Firewall • Load Balancer • Aya (Rust)
Prerequisite: Module 0 complete — C programming basics recommended
Day 1
XDP & TC
Packet filtering, DDoS, LB, QoS
Day 2
eBPF Development
libbpf C, Aya Rust, unit testing

## Slide 2
Track C: Overview
D1-1
XDP Architecture
Packet path, XDP hooks, program types
Return codes: PASS, DROP, TX, REDIRECT
45 min
D1-2
eBPF Firewall & DDoS
L3/L4 firewall, SYN flood mitigation
IP allowlist/blocklist with maps
45 min
D1-3
Load Balancer & QoS
Stateless LB via bpf_redirect
TC ingress/egress, traffic shaping
45 min
D2-1
libbpf C Deep Dive
Skeleton API, CO-RE, error handling
BPF ring buffer consumer
45 min
D2-2
eBPF in Rust with Aya
Aya framework, maps, programs
Cargo xtask build workflow
45 min
D2-3
Testing & CI
bpf_testmod, network namespaces
CI integration, sanitizers
45 min

## Slide 3
XDP Architecture: where packets meet eBPF
XDP (eXpress Data Path) hooks into the driver layer before the kernel network stack — the earliest possible point.
▶
NIC
Driver
▶
XDP
Hook
▶
Traffic
Control (TC)
▶
IP Stack
(netfilter)
Socket
(userspace)
XDP return codes:
Return code | Action | Use case
XDP_PASS | Forward packet to network stack | Normal flow
XDP_DROP | Drop packet at driver level | < 1µs — lowest overhead
XDP_TX | Retransmit from same interface | Reflection, NAT
XDP_REDIRECT | Forward to another interface/CPU | Load balancing, DPDK-style
XDP_ABORTED | Error — drop with trace | Debug only
Attachment modes:
Generic (skb)
Kernel fallback, no driver support needed. Slower.
Native
Driver-level hook. Full performance.
Offloaded
Runs on SmartNIC hardware. Fastest.

## Slide 4
XDP Firewall: L3/L4 packet filtering
xdp_firewall.bpf.c
// XDP L3/L4 firewall with IP blocklist map
struct { __uint(type, BPF_MAP_TYPE_LPM_TRIE);
__uint(max_entries, 1024);
__type(key, struct bpf_lpm_trie_key_u8);
__type(value, u32); } blocklist SEC(".maps");
SEC("xdp")
int xdp_firewall(struct xdp_md *ctx) {
void *data = (void *)(long)ctx->data;
void *data_end = (void *)(long)ctx->data_end;
struct ethhdr *eth = data;
if ((void*)(eth+1) > data_end) return XDP_PASS;
if (eth->h_proto != bpf_htons(ETH_P_IP)) return XDP_PASS;
struct iphdr *ip = (void*)(eth+1);
if ((void*)(ip+1) > data_end) return XDP_DROP;
// LPM lookup: block entire subnets
struct { u32 prefixlen; u32 addr; } key = {32, ip->saddr};
if (bpf_map_lookup_elem(&blocklist, &key))
return XDP_DROP;
return XDP_PASS;
}
SYN flood mitigation:
syn_flood.bpf.c
// Count SYN packets per source IP
// Drop if rate > threshold
struct { __uint(type, BPF_MAP_TYPE_LRU_HASH);
__uint(max_entries, 65536);
__type(key, u32); __type(value, u64);
} syn_count SEC(".maps");
#define SYN_THRESHOLD 1000
// In XDP program body:
if (tcp->syn && !tcp->ack) {
u64 *cnt = ...; // lookup src IP
if (cnt && *cnt > SYN_THRESHOLD)
return XDP_DROP;
}
Key XDP context fields:
ctx->data
Pointer to start of packet
ctx->data_end
Pointer to end (bounds check!)
ctx->ingress_ifindex
Incoming interface index
ctx->rx_queue_index
RX queue number

## Slide 5
Minimal eBPF Load Balancer with bpf_redirect
A userspace-free L4 load balancer: XDP receives the packet, rewrites MAC/IP, and redirects to a backend — no socket overhead.
lb_xdp.bpf.c
// Round-robin LB: pick backend from array map
struct backend { __u32 ip; __u8 mac[6]; __u32 ifindex; };
struct { __uint(type, BPF_MAP_TYPE_ARRAY);
__uint(max_entries, 8);
__type(key, u32); __type(value, struct backend);
} backends SEC(".maps");
struct { __uint(type, BPF_MAP_TYPE_PERCPU_ARRAY);
__uint(max_entries, 1);
__type(key, u32); __type(value, u32);
} rr_counter SEC(".maps");
SEC("xdp")
int lb_xdp(struct xdp_md *ctx) {
// Increment per-CPU counter
u32 k=0, *cnt = bpf_map_lookup_elem(&rr_counter, &k);
if (!cnt) return XDP_PASS;
u32 idx = __sync_fetch_and_add(cnt, 1) % 8;
// Get backend
struct backend *b = bpf_map_lookup_elem(&backends, &idx);
if (!b) return XDP_PASS;
// Rewrite destination MAC + redirect
__builtin_memcpy(eth->h_dest, b->mac, ETH_ALEN);
return bpf_redirect(b->ifindex, 0);
}
vs userspace LB:
 | eBPF XDP | HAProxy/nginx
Packet path | Driver → redirect | Kernel → socket → userspace → socket
Latency | < 2µs | 50-500µs
CPU cost | Near-zero | 1 core per ~100k rps
State | BPF maps | Process memory
Reload | bpf map update | Process restart
TC vs XDP
TC (Traffic Control) hooks after the network stack — supports both ingress and egress, and can modify existing sockets. Use TC for QoS, shaping and egress policies.

## Slide 6
TC eBPF: Traffic shaping and QoS
attach_tc.sh
# Attach TC program to ingress clsact
tc qdisc add dev eth0 clsact
tc filter add dev eth0 ingress bpf \
obj tc_prog.bpf.o sec classifier direct-action
# Inspect active filters
tc filter show dev eth0 ingress
tc_rate_limit.bpf.c
// TC program: rate limit specific traffic
SEC("classifier")
int tc_rate_limit(struct __sk_buff *skb) {
// Access packet via skb->data / skb->data_end
// Same bounds checking rules as XDP
u32 src_ip = ...; // parse IP header
// Token bucket: check rate per source IP
struct token_bucket *tb = lookup(&buckets, &src_ip);
if (!tb || tb->tokens == 0)
return TC_ACT_SHOT; // drop
tb->tokens--;
return TC_ACT_OK; // pass
}
TC action codes:
Action | Value | Effect
TC_ACT_OK | 0 | Pass packet to next stage
TC_ACT_SHOT | 2 | Drop packet
TC_ACT_REDIRECT | 7 | Redirect to another interface
TC_ACT_PIPE | 3 | Continue to next filter
XDP vs TC summary:
Feature | XDP | TC
Hook point | Driver (pre-stack) | After qdisc
Egress | No | Yes (clsact)
skb access | No (raw) | Yes (sk_buff)
Performance | Highest | High
Complexity | Lower | Higher

## Slide 7
DAY 2
eBPF Development
libbpf C • Skeleton API • Aya (Rust) • Unit testing
libbpf C
Skeleton, CO-RE, ringbuf
Aya
Rust, Cargo, safe maps
Testing
bpf_testmod, namespaces
CI/CD
Sanitizers, coverage

## Slide 8
libbpf Skeleton API: the modern way
BPF skeletons are auto-generated C headers that give type-safe access to all maps and programs defined in your .bpf.c file.
prog_loader.c
// 1. Generate skeleton (once, in Makefile):
// bpftool gen skeleton prog.bpf.o > prog.skel.h
// 2. Userspace loader — fully typed, no error-prone strings
#include "prog.skel.h"
int main() {
struct prog_bpf *skel = prog_bpf__open();
if (!skel) { perror("open"); return 1; }
// Configure before load (e.g. set global vars)
skel->rodata->my_pid = getpid();
if (prog_bpf__load(skel)) { perror("load"); goto cleanup; }
if (prog_bpf__attach(skel)) { perror("attach"); goto cleanup; }
// Consume events from ring buffer
struct ring_buffer *rb = ring_buffer__new(
bpf_map__fd(skel->maps.events),
handle_event, NULL, NULL);
while (!exiting)
ring_buffer__poll(rb, 100 /* timeout ms */);
cleanup:
prog_bpf__destroy(skel);
}
Key skeleton API calls:
prog_bpf__open()
Allocate and open BPF object
Reads ELF, resolves BTF maps
prog_bpf__load()
Verifies and JIT-compiles
Loads all programs and maps
prog_bpf__attach()
Attaches all auto-attachable
programs to their hooks
prog_bpf__destroy()
Detaches, unloads, frees
all resources
Makefile tip: add bpftool gen skeleton prog.bpf.o > prog.skel.h as a dependency of prog.c

## Slide 9
eBPF in Rust with Aya
Aya is a pure-Rust eBPF library: both the kernel program and the userspace loader are written in Rust, with no LLVM dependency at runtime.
myapp-ebpf/src/main.rs
// eBPF kernel program (src/main.rs in myapp-ebpf crate)
#![no_std]
#![no_main]
use aya_ebpf::{macros::tracepoint, programs::TracePointContext};
use aya_log_ebpf::info;
#[tracepoint]
pub fn myapp(ctx: TracePointContext) -> u32 {
match try_myapp(ctx) {
Ok(ret) => ret,
Err(_) => 1,
}
}
fn try_myapp(_ctx: TracePointContext) -> Result<u32, u32> {
info!(&ctx, "tracepoint hit!");
Ok(0)
}
myapp/src/main.rs
// Userspace loader (src/main.rs in myapp crate)
use aya::Bpf;
use aya::programs::TracePoint;
#[tokio::main]
async fn main() -> Result<(), anyhow::Error> {
let mut bpf = Bpf::load(include_bytes_aligned!(
"../../target/bpfel-unknown-none/release/myapp"))?;
let program: &mut TracePoint =
bpf.program_mut("myapp").unwrap().try_into()?;
program.load()?;
program.attach("syscalls", "sys_enter_execve")?;
tokio::signal::ctrl_c().await?;
Ok(())
}
Why Aya: memory safety in userspace • no LLVM at runtime (binary is self-contained) • async-native (Tokio) • full BTF/CO-RE support

## Slide 10
Testing eBPF programs
eBPF programs run in the kernel — testing requires special infrastructure. Three complementary approaches.
1
bpf_prog_test_run()
Kernel syscall: feed synthetic packets or syscall events directly to the eBPF program. No network interface needed. Fast and reproducible.
BPF_PROG_TEST_RUN / bpf_prog_test_run_opts()
> Feed synthetic __sk_buff or xdp_md
> Check XDP_DROP / XDP_PASS return code
> Validate map state after program run
2
Network namespaces
Create isolated network namespace, attach XDP program, send packets with veth pair. Tests full kernel integration including driver hooks.
ip netns add test-ns
ip link add veth0 type veth peer veth1
ip link set veth1 netns test-ns
# attach XDP, run test traffic via veth
3
Sanitizers in CI
Run bpftool prog load with --log-level 2 in CI. Use asan/ubsan on userspace loader. Check verifier log in automated tests.
sudo bpftool prog load prog.bpf.o /dev/null \
--log-level 2 2>&1 | grep -E 'ERROR|INVALID'
# Exit 0 = verifier accepted
# Exit 1 = verifier rejected (CI fail)

## Slide 11
SUMMARY
Track C: Key takeaways
XDP
Driver-level hook
Return: PASS DROP TX REDIRECT
Generic / Native / Offloaded
XDP Firewall
LPM trie for subnet blocks
LRU hash for SYN rate limiting
bpf_map_lookup + XDP_DROP
LB / Redirect
bpf_redirect() for zero-copy
Round-robin via PERCPU_ARRAY
MAC rewrite in program body
TC
After network stack (ingress+egress)
QoS, shaping, policing
TC_ACT_OK / TC_ACT_SHOT
libbpf Skeleton
Type-safe auto-generated API
prog__open → load → attach
ring_buffer__poll for events
Aya (Rust)
Pure Rust kernel + userspace
No LLVM at runtime
Async-native with Tokio
Next: Track D — Debugging & Runtimes: uprobes • USDT • black-box debugging • chaos engineering